## Slide 1
IoT-Based Weather Monitoring System
Using NodeMCU ESP8266
An Embedded Systems Mini Project
Team MEMBERS:
S20240020285
S20240020314
S20240020315

## Slide 2
Project Objective
This project aims to design and develop a comprehensive IoT-based weather monitoring system that captures critical environmental data including temperature, humidity, rainfall, and light intensity. The system transmits this data in real-time to the Blynk cloud platform, enabling users to monitor weather conditions remotely from anywhere using a smartphone application. By combining embedded systems with cloud connectivity, this project demonstrates practical IoT implementation for real-world environmental sensing applications.

## Slide 3
Why Weather Monitoring Matters
Agriculture & Farming
Optimize irrigation schedules and crop management based on real-time environmental data
Smart Cities
Monitor urban climate conditions for traffic management, pollution control, and public safety
Environmental Protection
Track ecological conditions and detect anomalies for conservation efforts
Weather monitoring is essential across multiple domains. This system leverages NodeMCU ESP8266's Wi-Fi capabilities to collect sensor data continuously and transmit it to the Blynk cloud platform, enabling anywhere, anytime access through a mobile application. The integration of multiple sensors provides comprehensive environmental insights that support decision-making in agriculture, urban planning, and environmental science.

## Slide 4
Hardware Components
1
NodeMCU ESP8266
Wi-Fi enabled microcontroller with built-in IoT capabilities for data collection and transmission
2
DHT11 Sensor
Digital temperature and humidity sensor providing accurate environmental readings
3
Rain Sensor
Detects precipitation and measures rainfall intensity through analog output
4
LDR Sensor
Light Dependent Resistor measures ambient light intensity for solar radiation data
5
BMP180 Sensor
The BMP180 is a digital sensor used to measure atmospheric pressure and temperature. It communicates via the I²C interface and provides highly accurate data for weather monitoring and altitude calculation.
6
Supporting Components
Breadboard for prototyping, jumper wires for connections, and power supply (3.3V)

## Slide 5
System Architecture
Real-time Environmental Monitoring
An IoT system for tracking environmental conditions
Data Processing
NodeMCU ESP8266 aggregates and processes sensor inputs
Cloud Transmission
Wi-Fi sends processed data to the Blynk Cloud platform
Sensor Data Collection
DHT11, Rain, and LDR sensors gather environmental data
Mobile Visualization
Real-time display of environmental data on a mobile app
The system follows a modular architecture where distributed sensors collect environmental parameters. The NodeMCU ESP8266 acts as the central processing unit, aggregating sensor readings and managing Wi-Fi communication. Data packets are transmitted securely to the Blynk cloud platform, which stores and visualizes the information for user access through mobile and web applications.

## Slide 6
Circuit Connections & Pin Configuration
Sensor Component
Pin Connection
Notes
DHT11 (Data)
GPIO D4 (Pin 2)
Digital signal with internal pull-up required
Rain Sensor (Analog Out)
A0 (ADC)
Analog input, 0-1023 range
LDR Sensor (Analog Out)
A0 (ADC) via MUX
Can be multiplexed or use separate channel
Power Supply (VCC)
3.3V
Regulated power for all components
Ground Reference
GND
Common ground for all circuits

## Slide 7
Operating Principle
Environmental Sensing
Distributed sensors continuously detect temperature, humidity, rainfall, and light intensity from the environment
Data Collection
NodeMCU reads analog and digital signals from sensors via GPIO pins and ADC converter
Processing & Validation
Microcontroller processes raw sensor values, applies calibration, and validates data quality
Cloud Transmission
Data is formatted and transmitted to Blynk servers via Wi-Fi at regular intervals
Real-Time Visualization
Blynk app displays live readings using interactive gauges, graphs, and numerical displays

## Slide 8
Software Development Environment
Arduino IDE
Integrated development environment for writing, compiling, and uploading firmware to NodeMCU boards with ESP8266 board support
Blynk Mobile App
Cross-platform application for iOS and Android enabling real-time data visualization and remote device control
Required Libraries
ESP8266WiFi.h (Wi-Fi connectivity), BlynkSimpleEsp8266.h (cloud integration), DHT.h (sensor communication)

## Slide 9
Firmware Implementation
Key Programming Steps:
1
Initialize Wi-Fi Connection
Configure SSID, password, and establish connection to local network using WiFi.begin()
2
Authenticate with Blynk
Set authentication token and initiate connection to Blynk server through Blynk.connect()
3
Read Sensor Data
Continuously sample DHT11 digital output and convert analog signals from rain/LDR sensors
4
Process & Format Data
Apply sensor calibration coefficients and format values for transmission to virtual pins
5
Periodic Cloud Sync
Send aggregated sensor data to Blynk virtual pins at configurable intervals (typically 10-30 seconds)

## Slide 10
System Output & Real-World Applications
Blynk Dashboard Features
  Gauge Widgets: Analog displays for temperature and humidity ranges
  Graph Visualization: Historical data trends over hours or days
  LED Indicators: Visual alerts for threshold violations
  Numeric Displays: Real-time values with units and precision
Practical Applications
  Smart Agriculture: Automated irrigation scheduling based on rainfall and humidity
  Environmental Monitoring: Pollution tracking and ecological impact assessment
  Smart Homes: Climate control and energy optimization
  Educational Stations: Weather monitoring infrastructure for schools

## Slide 11
THANK YOU.
We appreciate your attention to our presentation on the IoT Weather Monitoring Project. Here's a brief summary of the key components and their impact:
IoT Core: NodeMCU ESP8266
The foundation of our system, leveraging the powerful ESP8266 for efficient data processing and connectivity.
Sensor Integration
Seamlessly integrated environmental sensors for accurate real-time data acquisition of temperature, humidity, and more.
Cloud Connectivity via Blynk
Utilizing Blynk for robust cloud integration, enabling remote monitoring and intuitive dashboard visualization of data.
Real-World Impact
From smart agriculture to environmental monitoring, our system provides actionable insights for diverse practical applications.